## Slide 1: RISC-V Soft Processor on PolarFire

## Slide 2: What is RISC-V
A New free and open ISA developed at UC Berkeley
  RISC-V is “Instruction set architecture” (ISA). Not a processor.
  The micro architecture implementations can be open or proprietary
  Can expand to have open specifications for platforms, accelerators etc.
  Permits reuse of the Software across many micro architectures
  Goal is to encourage both open-source and proprietary implementations of the RISC-V ISA specification
Designed for
  Research, Education & Commercial use
RISC-V foundation
  Directs future development and foster adoption
  https://riscv.org/

## Slide 3: Frozen RISC-V Base & Extensions
Four base integer ISA Variants
  RV32I, RV64I, RV32E, RV128I (32, 64, 128 bit machines)
  I : Base Integer instruction set
Standard extensions - All frozen in 2014 – Forever
  M: Integer multiply/divide
  A: Atomic memory operations
  F: Single Precision Floating Point
  D: Double Precision Floating Point
  G: IMAFD, General purpose ISA
  Q: Quad Precision Floating Point
  C: 16-bit Compressed instruction (RV32C, RV64C)
Future extension
  V: Vector extensions – in definition

## Slide 4: RISC-V Privileged Architecture
Four privilege modes
  User mode – U
  Supervisor mode – S
  Hypervisor mode – H // not specified yet
  Machine mode – M
Supported combinations
  M // simple embedded
  M, U // embedded with protection
  M, S, U // operating systems
  M, H, S, U // systems running hypervisors
Expect ratification CQ2

## Slide 5: RISC-V Soft Processor on PolarFire
CoreRISCV_AXI4
  Based on SiFive’s Coreplex E31 design
  Will be available through Libero Catalog
    IP Core
    CoreRISCV_AXI4 Handbook
    CoreRISCV_AXI4 release note
    RISC-V privileged ISA spec
    RISC-V user level ISA Spec
Key Features
  Supports the RISC-V standard RV32IM ISA
  Integrated 8Kbytes instructions cache and 8 Kbytes data cache
  Two external AXI interfaces for IO and memory
  Support up to 31 programmable interrupts
  Debug unit with a JTAG interface
  Best suited for low-mid range Microcontroller applications

## Slide 6: CoreRISCV_AXI4
Block Diagram

## Slide 7: CoreRISCV_AXI4
CoreRISCV_AXI4 Processor Core
  Based on the E31 Coreplex Core by SiFive
  Provides a single hardware thread (hart) (one PC + one set of Registers)
  Machine-mode privileged architecture
  Supports the RISCV standard RV32IM ISA
      “I” stands for “Base Integer”
      “M” stands for “Integer Multiplication and Division”

## Slide 8: CoreRISCV_AXI4
Two External AXI interfaces
  AXI memory interface
      Cached access to instruction and data memory
  AXI I/O interface
      Un-cached accesses to I/O peripherals
Memory System
  First-level instruction cache
      The instruction cache is 8 KB
      Direct-mapped with a 64 bytes line size.
      One Clock cycle Access latency.
  First-level data cache
      The data cache size is 8 KB,
      Direct-mapped with a line size of 64 bytes.
      The access latency is two clock cycles for full words and three clock cycles for smaller quantities.
  Un-cached memory access for I/O

## Slide 9: CoreRISCV_AXI4
Interrupt Sources
  Local Interrupts
    Wired directly to the CPU internally
    Standard software interrupts (Exceptions , traps)
    Timer interrupt
  Global interrupts
    Routed via Platform-Level Interrupt Controller(PLIC)
    Supports up to 31 external interrupt sources
    All external interrupts are single priority level at priority 1.
    Supports Level triggered interrupts
    External interrupts in the system can be connected here.

## Slide 10: CoreRISCV_AXI4
JTAG Interface
  Industry-standard 1149.1 JTAG interface
  Supports Interactive debug
  Supports Hardware breakpoints (maximum 2)
  Accessible via FlashPro5 JTAG programmer/Debugger
  Unlike CoreCortexM1, UJTAG module is not part of CoreRISCV_AXI4
  Use CoreJTAGDebug for JTAG access

## Slide 11: CoreJTAGDebug
Key Features
    Facilitates JTAG interface to soft processor CoreRISCV_AXI4
    Provides fabric access to the JTAG interface
    Configurable IR Code support for JTAG tunneling
      Allows debug support for multiple soft-processors
    Future version is aimed towards debug support for multiple soft-processors

## Slide 12: CoreRISCV_AXI - SoftConsole
SoftConsole 5.0
  Installer available here
  Works with FlashPro5.
  Supported platforms
    Ubuntu 14.04.5 LTS Desktop 32 and 64 bit
    Ubuntu 16.04.1 LTS Desktop 32 and 64 bit
    CentOS/Red Hat Enterprise Linux 6.8 Desktop 32 and 64 bit
    CentOS/Red Hat Enterprise Linux 7.2 Desktop 64 bit
    OpenSuse Leap 42.1 [Gnome/Kde desktop] 64 bit
  Platforms not supported yet
    Linux distributions/versions other than those listed above
    Microsoft Windows
    Virtual machines
  Release note available here
    Installation instruction
    Known issues

## Slide 13: CoreRISCV_AXI - SoftConsole
Firmware project structure
  hal
      Hardware abstraction layer
      Same as CortexM3 HAL on SmartFusion2
      Register accesses e.g. HAL_set_32bit_reg
  riscv_hal
      RISCV Startup code
      PLIC control
      Equivalent to CMSIS on CortexM3 HAL on SmartFusion2
  drivers
      user peripheral drivers e.g. CoreSPI, CoreGPIO
riscv_hal is available on github
  https://github.com/RISCV-on-Microsemi-FPGA/riscv-hal

## Slide 14: CoreRISCV_AXI4 system on PolarFire
CoreRISCV_AXI4
CoreAXIToAHB
CoreAHBL
CoreAHBtoAPB
CoreAPB
CoreGPIO
CoreTimer
CoreSPI
AXI_MST_MEM
CoreAXI4Interconnect
AXI_MST_MMIO
PLIC Interrupts
JTAG
Clock
Reset
CoreJTAGDebug
CoreAXI4SRAM

## Slide 15: CoreRISCV_AXI4 – Booting the system
Boot options
    Debug Mode
        Executing code from LSRAM using JTAG
    Release mode
        Design Initialization using PolarFire System Controller
          Image can reside in sNVM, uPROM, or SPI-Flash
            At power-up the image is loaded into LSRAM.
            Image is then executed out of LSRAM.
            Able to select locations post P&R
        CoreBootStrap
            Hardware boot-loader
            Loads image into LSRAM from SPI-Flash using soft logic

## Slide 16: Booting CoreRISCV_AXI4 on PolarFire
FlashPro5 connected to JTAG port for interactive debug
Download image to CoreAXI4SRAM connected on the CoreRISCV_AXI4 code memory space
After reset CoreRISCV_AXI4 fetches and executes code from CoreAXI4SRAM
Debug Mode:
CoreRISCV_AXI4
AXI_MST_MEM
CoreAXIToAHB
CoreAHBL
CoreAHBtoAPB
CoreAPB
CoreGPIO
CoreTimer
CoreSPI
AXI_MST_MMIO
JTAG
CoreJTAGDebug
CoreAXI4Interconnect
CoreAXI4SRAM

## Slide 17: Booting CoreRISCV_AXI4 on PolarFire
Connect CoreAXI4SRAM on code memory space of CoreRISCV_AXI4 memory map.
Use CoreBootStrap IP as first level Boot loader
The CoreBootStrap Holds the CoreRISCV_AXI4 in reset while it copies the application executable from on-board SPI Flash memory to CoreAXI4SRAM after system reset.
Application executable should be pre-loaded on the SPI Flash memory.
Releases reset on CoreRISCV_AXI4 after completion of copying executable to CoreAXI4SRAM
CoreRISCV_AXI4 now fetches and executes code from CoreAXI4SRAM.
CoreBootStrap
CoreRISCV_AXI4
CoreAXIToAHB
CoreAHBL
CoreAHBtoAPB
CoreAPB
CoreGPIO
CoreTimer
CoreSPI
AXI_MST_MMIO
RESET
CoreSPI
On-Board
SPI Flash
AXI_MST_MEM
CoreBootstrap:
CoreAXI4Interconnect
CoreAXI4SRAM
AHB Master
AXI Master

## Slide 18: Booting CoreRISCV_AXI4 on PolarFire
Connect CoreAXI4SRAM on code memory space of CoreRISCV_AXI4 memory map.
Use the configurator of CoreAXI4SRAM to attach a memory initialization file to it. This file should contain the application executable.
Use the Libero “Design and memory Initialization” GUI post P&R
The memory client will be stored on chosen memory, e.g. sNVM, uPROM etc. Memory client will be part of bit-stream output of the Libero design.
On system reset, System Controller will initialize the destination CoreAXI4SRAM with memory client from chosen memory.
The CoreRISCV_AXI4 will now execute application executable from CoreAXI4SRAM after it comes out of reset.
CoreRISCV_AXI4
CoreAXIToAHB
CoreAHBL
CoreAHBtoAPB
CoreAPB
CoreGPIO
CoreTimer
CoreSPI
AXI_MST_MMIO
Attach application executable as memory client to the RAM using Libero
Design Initialization
CoreAXI4Interconnect
CoreAXI4SRAM
AXI_MST_MEM

## Slide 19: Booting CoreRISCV_AXI4 on PolarFire
Connect CoreAXI4SRAM_1 in the code memory space of CoreRISCV_AXI4 memory map.
Use the configurator of CoreAXI4SRAM_1 to attach a memory initialization file to it. This file should contain the first level boot loader executable code.
Use the Libero “Design and memory Initialization” GUI post P&R
The memory client will be stored on chosen memory, e.g. sNVM, uPROM etc. Memory client will be part of bit-stream output of the Libero design.
At system initialization time, System Controller will initialize the destination CoreAXI4SRAM_1 with memory client from chosen memory.
The CoreRISCV_AXI4 will now execute first level boot loader from CoreAXI4SRAM_1 after it comes out of reset.
The boot loader functionality is to copy application executable from on-board SPI Flash memory to CoreAXI4SRAM_2.
After copy, the CoreRISCV_AXI4 jumps to address of CoreAXI4SRAM_2 to start executing the application image.
Application executable should be pre-loaded on the SPI Flash memory.
The base addresses of CoreAXI4SRAM_1, CoreAXI4SRAM_2 and the linker scripts of both executable codes must be coordinated to point to correct memory map.
CoreRISCV_AXI4
CoreAXIToAHB
CoreAHBL
CoreAHBtoAPB
CoreAPB
CoreGPIO
CoreTimer
CoreSPI
AXI_MST_MMIO
CoreAXI4Interconnect
CoreAXI4SRAM_1
AXI_MST_MEM
Attach first level boot-loader executable as memory client to the RAM using Libero
Design Initialization
  – two stage firmware boot
On-Board
SPI Flash
CoreAXI4SRAM_2
CoreSPI

## Slide 20
Thank you